INSTALLATION INSTRUCTIONS

2nd-3rd Gen Conversion Bracket

- Remove track bar and ball-stud from frame lug.

- Drill or ream 3/4” taper bore in frame lug to 3/4” straight bore.

- Straddle frame lug with conversion bracket, insert 3/4” bolt upwards through entire bracket & assemble flat washer, lock washer & nut to bolt.

- Mount new track bar into axle bracket.

- Insert driver’s side track bar bolt through conversion bracket (CB), toothed washers (TW) & flat washers (FW) in the following order: TW*CB*TW*bushing*FWs*TW*CB*TW*flag nut.

- Fully thread bolt through flag nut (avoid cross-threading).

- Tighten 3/4” nut on frame lug to collapse split-ring lock washer.

- Assemble 1/2” bolt to bracket & frame tab (not found on early 2nd Gen Rams) - stainless steel washer under bolt head, sleeve spacer above bracket tab and flat washers, nuts & split-ring lock washer to capture frame tab.

- Use 1/2” washers to adjust spacer length as needed & tighten 1/2” nuts to collapse split-ring lock washer.

- Torque axle end track bar bolt to 155 ft-lbs. (more if not using Ultimate Hardware Kit).

- Torque 3/4” nut to 175 ft-lbs.

- Torque frame end track bar bolt to 155 ft-lbs.

LazarSmith©